## Slide 1: Computer Networks
Rabea Khatun
Lecturer
Dept. Of CSE
East West University
CSE405
Network Layer

## Slide 2: Network-layer services and protocols
transport segment from sending to receiving host
  sender: encapsulates segments into datagrams, passes to link layer
  receiver: delivers segments to transport layer protocol
network layer protocols in every Internet device: hosts, routers
routers:
  examines header fields in all IP datagrams passing through it
  moves datagrams from input ports to output ports to transfer datagrams along end-end path
mobile network
enterprise
network
national or global ISP
datacenter
network
application
transport
network
link
physical
application
transport
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical
network
link
physical

## Slide 3: Two key network-layer functions
network-layer functions:
forwarding: move packets from a router’s input link to appropriate router output link
analogy: taking a trip
forwarding: process of getting through single interchange
forwarding
routing
routing: process of planning trip from source to destination
routing: determine route taken by packets from source to destination
  routing algorithms

## Slide 4: Network layer: data plane, control plane
Data plane:
local, per-router function
determines how datagram arriving on router input port is forwarded to router output port
Control plane
network-wide logic
determines how datagram is routed among routers along end-end path from source host to destination host
1
2
3
0111
values in arriving
packet header

## Slide 5: Per-router control plane
Individual routing algorithm components in each and every router interact in the control plane
Routing
Algorithm
data
plane
control
plane
1
2
0111
values in arriving
packet header
3

## Slide 6: Connection, connection-less service
datagram network provides network-layer connectionless service
virtual-circuit network provides network-layer connection service
analogous to TCP/UDP connecton-oriented / connectionless transport-layer services, but:
  service: host-to-host
  no choice: network provides one or the other
  implementation: in network core

## Slide 7: Virtual circuits
call setup, teardown for each call before data can flow
each packet carries VC identifier (not destination host address)
link, router resources (bandwidth, buffers) may be allocated to VC (dedicated resources = predictable service)
“source-to-dest path behaves much like telephone circuit”

## Slide 8: VC implementation
a VC consists of:
  path from source to destination
  VC numbers, one number for each link along path
  entries in forwarding tables in routers along path
packet belonging to VC carries VC number (rather than dest address)
VC number can be changed on each link.
  new VC number comes from forwarding table

## Slide 9: VC forwarding table
12
22
32
1
2
3
VC number
interface
number
Incoming interface Incoming VC # Outgoing interface Outgoing VC #
1 12 3 22
2 63 1 18
3 7 2 17
1 97 3 87
… … … …
forwarding table in
northwest router:
VC routers maintain connection state information!

## Slide 10: Virtual circuits: signaling protocols
application
transport
network
data link
physical
used to setup, maintain teardown VC
used in ATM, frame-relay, X.25
not used in today’s Internet
1. initiate call
2. incoming call
3. accept call
4. call connected
5. data flow begins
6. receive data
application
transport
network
data link
physical

## Slide 11: Datagram networks
no call setup at network layer
routers: no state about end-to-end connections
  no network-level concept of “connection”
packets forwarded using destination host address
1. send datagrams
application
transport
network
data link
physical
application
transport
network
data link
physical
2. receive datagrams

## Slide 12: Datagram forwarding table
1
2
3
IP destination address in
arriving packet’s header
routing algorithm
local forwarding table
dest address
output link
address-range 1
address-range 2
address-range 3
address-range 4
3
2
2
1
4 billion IP addresses, so rather than list individual destination address
list range of addresses
(aggregate table entries)

## Slide 13: Datagram forwarding table
Destination Address Range
11001000 00010111 00010000 00000000
through
11001000 00010111 00010111 11111111
11001000 00010111 00011000 00000000
through
11001000 00010111 00011000 11111111
11001000 00010111 00011001 00000000
through
11001000 00010111 00011111 11111111
otherwise
Link Interface
0
1
2
3
Q: but what happens if ranges don’t divide up so nicely?

## Slide 14: Destination-based forwarding
Q: but what happens if ranges don’t divide up so nicely?
3
Notes: Text for this animation:
This all works out pretty nice and looks pretty simple!
But of course the devil is in the details, as the saying goes.
What happens, for example, when a subset of addresses say in this first range should go to say interface 3, rather than interface 0. Well, of course we could split the first address range into multiple pieces, and add in this new subrange with its new destination output port. But it turns out there’s a much simpler and elegant way to do this. Known as longest prefix matching.

## Slide 15: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
********
***
********
***
********
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
11001000 00010111 00010110 10100001

## Slide 16: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 17: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 18: Longest prefix matching
when looking for forwarding table entry for given destination address, use longest address prefix that matches destination address.
longest prefix match
Destination Address Range
11001000 00010111 00010
11001000 00010111 00011000
11001000 00010111 00011
otherwise
Link interface
0
1
2
3
11001000 00010111 00011000 10101010
examples:
which interface?
which interface?
********
***
********
***
********
11001000 00010111 00010110 10100001
match!

## Slide 19: IP Datagram format
ver
length
32 bits
payload data
(variable length,
typically a TCP
or UDP segment)
16-bit identifier
header
checksum
time to
live
source IP address
head.
len
type of
service
flgs
fragment
offset
upper
layer
destination IP address
options (if any)
IP protocol version number
header length(bytes)
upper layer protocol (e.g., TCP or UDP)
total datagram
length (bytes)
“type” of service:
fragmentation/
reassembly
TTL: remaining max hops
(decremented at each router)
e.g., timestamp,
32-bit source IP address
32-bit destination IP address
header checksum

## Slide 20: IP fragmentation/reassembly
network links have MTU (max. transfer size) - largest possible link-level frame
  different link types, different MTUs
large IP datagram divided (“fragmented”) within net
  one datagram becomes several datagrams
  “reassembled” only at destination
  IP header bits used to identify, order related fragments
fragmentation:
in: one large datagram
out: 3 smaller datagrams
reassembly
…
…

## Slide 21: IP fragmentation/reassembly
ID
=x
offset
=0
fragflag
=0
length
=4000
ID
=x
offset
=0
fragflag
=1
length
=1500
ID
=x
offset
=185
fragflag
=1
length
=1500
ID
=x
offset
=370
fragflag
=0
length
=1040
one large datagram becomes
several smaller datagrams
example:
4000 byte datagram
MTU = 1500 bytes
1480 bytes in data field
offset =
1480/8

## Slide 22: IP addressing: introduction
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
IP addresses associated with each interface
Written in dotted-decimal notations
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:

## Slide 23: IP addressing: introduction
IP address: 32-bit identifier associated with each host or router interface
interface: connection between host/router and physical link
  router’s typically have multiple interfaces
  host typically has one or two interfaces (e.g., wired Ethernet, wireless 802.11)
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.1 = 11011111 00000001 00000001 00000001
223
1
1
1
dotted-decimal IP address notation:

## Slide 24: IP addressing
Binary Notation
Hexadecimal Notation

## Slide 25: IP addressing

## Slide 26: IP addressing (Classful Addressing)

## Slide 27
Find the class of each address.
a. 00000001 00001011 00001011 11101111
b. 11000001 10000011 00011011 11111111
c. 14.23.120.8
d. 252.5.15.111
Example
Solution
a. The first bit is 0. This is a class A address.
b. The first 2 bits are 1; the third bit is 0. This is a class C address.
c. The first byte is 14; the class is A.
d. The first byte is 252; the class is E.

## Slide 28: IP addressing (Classful Addressing)
Exercise:

## Slide 29: IP addressing (Classful Addressing)
Solution:

## Slide 30: IP addressing (Classful Addressing)

## Slide 31: IP addressing (Classful Addressing)

## Slide 32
Problem
How can we prove that we have 2,147,483,648 addresses in class A?
Solution
In class A, only 1 bit defines the class. The remaining 31 bits are available for the address.
With 31 bits, we can have 231 or 2,147,483,648 addresses.

## Slide 33
Problem
Given the network address 17.0.0.0, find the class, the block, and the range of the addresses.
Solution
The class is A because the first byte is between 0 and 127. The block has a netid of 17 (00010001). The addresses range from 17.0.0.0 to 17.255.255.255.

## Slide 34
Problem
Given the network address 132.21.0.0, find the class, the block, and the range of the addresses.
Solution
The class is B because the first byte is between 128 and 191. The block has a netid of 132.21. The addresses range from 132.21.0.0 to 132.21.255.255.

## Slide 35
Problem
Given the network address 220.34.76.0, find the class, the block, and the range of the addresses.
Solution
The class is C because the first byte is between 192 and 223. The block has a netid of 220.34.76. The addresses range from 220.34.76.0 to 220.34.76.255.

## Slide 36: IP addressing (Classful Addressing)

## Slide 37: IP addressing (Classful Addressing)

## Slide 38: IP addressing (Classful Addressing)

## Slide 39: IP addressing (Classful Addressing)

## Slide 40: IP addressing (Classful Addressing)

## Slide 41: IP addressing: Classless Addressing
Classful addressing, which is almost obsolete, is replaced with classless addressing.
In classful addressing, a large part of the available addresses were wasted.
Note
Limitation of Classful Addressing

## Slide 42: How do we or devices identify the network part or the host part?
How do we or devices identify the network part or the host part?
Answer: For us :Using the “Prefix Mask”.
192.168.10.2/24 Means that the first 24 bits are the network portion. The last 8 bits are the host portion.

## Slide 43: How do we or devices identify the network part or the host part?
Answer: For devices Using the “subnet mask”.
255.255.255.0

## Slide 44: Prefix or Subnet Mask
The Prefix Mask and the Subnet Mask are different ways of representing the same information.
Prefix Mask of /24 or a subnet mask of 255.255.255.0
Prefix Mask of /16 or a subnet mask of 255.255.0.0
Prefix Mask of /8 or a subnet mask of 255.0.0.0

## Slide 45: Subnet Mask
IP Address: 10.24.36.2 / 8 Subnet Mask?
IP Address: 10.24.36.2 / 12 Subnet Mask?
IP Address: 10.24.36.2 / 16 Subnet Mask?
IP Address: 10.24.36.2 / 23 Subnet Mask?
IP Address: 10.24.36.2 255.255.224.0 Prefix Mask?
IP Address: 10.24.36.2 255.255.255.192 Prefix Mask?
IP Address: 10.24.36.2 255.255.255.252 Prefix Mask?
IP Address: 10.24.36.2 255.254.0.0 Prefix Mask?
IP Address: 10.24.36.2 255.255.240.0 Prefix Mask?

## Slide 46: IP addressing: CIDR
CIDR: Classless InterDomain Routing (pronounced “cider”)
  subnet portion of address of arbitrary length
  address format: a.b.c.d/x, where x is # bits in subnet portion of address
11001000 00010111 00010000 00000000
subnet
part
host
part
200.23.16.0/23

## Slide 47: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
What’s a subnet ?
  device interfaces that can physically reach each other without passing through an intervening router
network consisting of 3 subnets
IP addresses have structure:
  subnet part: devices in same subnet have common high order bits
  host part: remaining low order bits

## Slide 48: Subnets
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
Recipe for defining subnets:
detach each interface from its host or router, creating “islands” of isolated networks
each isolated network is called a subnet
subnet mask: /24
(high-order 24 bits: subnet part of IP address)
subnet
223.1.3.0/24
subnet 223.1.1.0/24
subnet 223.1.2.0/24

## Slide 49: Subnets
where are the subnets?
what are the /24 subnet addresses?
223.1.1.1
223.1.1.3
223.1.1.4
223.1.2.2
223.1.2.6
223.1.3.2
223.1.3.1
223.1.3.27
223.1.1.2
223.1.7.0
223.1.7.1
223.1.8.0
223.1.8.1
223.1.9.1
223.1.9.2
223.1.2.1
subnet 223.1.1/24
subnet 223.1.7/24
subnet 223.1.3/24
subnet 223.1.2/24
subnet 223.1.9/24
subnet 223.1.8/24

## Slide 50: IP addressing: CIDR
MASK
How do we know how many bits represent the network portion and how many bits represent the host portion?
The prefix length is the number of bits in the address that gives us the network portion. For example, in 172.16.4.0 /24, the /24 is the prefix length - it tells us that the first 24 bits are the network address.
another entity that is used to specify the network portion is called subnet mask. The subnet mask consists of 32 bits, just as the address does, and uses 1s and 0s to indicate which bits of the address are network bits and which bits are host bits.

## Slide 51: IP addressing (CIDR)
Solution
The binary representation of the given address is
11001111 00010000 00100101 00011000
For first addresses, we set (32−29) = 3 rightmost bits to 0, we get
11001111 00010000 00100101 00011000
For last addresses, we set (32 − 29) = 3 rightmost bits to 1, we get
11001111 00010000 00100101 00011111
The value of n is 29, which means that the range of the block is
2 32−29or 8.
So, There are only 8 addresses in this block

## Slide 52: IP addressing (CIDR)

## Slide 53: IP addressing (CIDR)
Subnetting allows for creating multiple logical networks from a single address block
Subnets are created using one or more of the host bits as network bits
  done by extending the mask to borrow some of the bits from the host portion to create additional network bits

## Slide 54: IP addressing (CIDR)
Calculating Subnets and Hosts
The number of subnets is calculated using 2n, where n is the number of bits borrowed
  21 = 2 subnets
  the more bits borrowed, the more subnets can be defined
The number of useable hosts per subnet is calculated using 2h - 2 where h is the number of host bits left
  27 – 2 = 126 useable hosts per subnet
  with each bit borrowed, fewer host addresses are available per subnet

## Slide 55: IP addressing (CIDR)
Subnetting Example 1
Need to borrow a minimum of 2 host bits.
  22 = 4 subnets

## Slide 56: IP addressing (CIDR)
Subnetting Example 2
Need to borrow a minimum of 3 host bits.
  23 = 8 subnets

## Slide 57: IP addressing (CIDR)

## Slide 58: IP addressing (CIDR)

## Slide 59: IP addressing (CIDR)

## Slide 60: IP addressing (CIDR)

## Slide 61: Example
IP address : 10.100.20.178 Subnet mask : 255.255.255.240 | 
Network | 
Broadcast | 
First usable host | 
Last usable host | 
number of usable host addresses | 
Given the IP address find the following information

## Slide 62: IP addressing (CIDR)

## Slide 63: IP addresses: how to get one?
Host address can be configured manually.
Q: How does a host get IP address?
hard-coded by system admin in a file
  Windows: control-panel->network->configuration->tcp/ip->properties
  UNIX: /etc/rc.config
DHCP: Dynamic Host Configuration Protocol: dynamically get address from as server
  “plug-and-play”
  DHCP allows a host to obtain an IP address automatically.

## Slide 64: DHCP: Dynamic Host Configuration Protocol
goal: host dynamically obtains IP address from network server when it “joins” network
  can renew its lease on address in use
  allows reuse of addresses (only hold address while connected/on)
  support for mobile users who join/leave network
DHCP overview:
  host broadcasts DHCP discover msg [optional]
  DHCP server responds with DHCP offer msg [optional]
  host requests IP address: DHCP request msg
  DHCP server sends address: DHCP ack msg

## Slide 65: DHCP client-server scenario
223.1.1.1
223.1.1.2
223.1.1.3
223.1.1.4
223.1.2.9
223.1.2.2
223.1.2.1
223.1.3.2
223.1.3.1
223.1.3.27
DHCP server
223.1.2.5
arriving DHCP client needs
address in this network
Typically, DHCP server will be co-located in router, serving all subnets to which router is attached

## Slide 66: DHCP client-server scenario
DHCP server: 223.1.2.5
Arriving client
DHCP discover
src : 0.0.0.0, 68
dest.: 255.255.255.255,67
yiaddr: 0.0.0.0
transaction ID: 654
DHCP offer
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 654
lifetime: 3600 secs
DHCP request
src: 0.0.0.0, 68
dest:: 255.255.255.255, 67
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
DHCP ACK
src: 223.1.2.5, 67
dest: 255.255.255.255, 68
yiaddrr: 223.1.2.4
transaction ID: 655
lifetime: 3600 secs
Broadcast: is there a DHCP server out there?
Broadcast: I’m a DHCP server! Here’s an IP address you can use
Broadcast: OK. I would like to use this IP address!
Broadcast: OK. You’ve got that IP address!
The two steps above can be skipped “if a client remembers and wishes to reuse a previously allocated network address” [RFC 2131]

## Slide 67: NAT: network address translation
10.0.0.1
10.0.0.2
10.0.0.3
10.0.0.4
local network (e.g., home network) 10.0.0/24
138.76.29.7
rest of
Internet
datagrams with source or destination in this network have 10.0.0/24 address for source, destination (as usual)
all datagrams leaving local network have same source NAT IP address: 138.76.29.7, but different source port numbers
NAT: all devices in local network share just one IPv4 address as far as outside world is concerned

## Slide 68: NAT: network address translation
  all devices in local network have 32-bit addresses in a “private” IP address space (10/8, 172.16/12, 192.168/16 prefixes) that can only be used in local network
  advantages:
    just one IP address needed from provider ISP for all devices
    can change addresses of host in local network without notifying outside world
    can change ISP without changing addresses of devices in local network
    security: devices inside local net not directly addressable, visible by outside world

## Slide 69: NAT: network address translation
implementation: NAT router must (transparently):
  outgoing datagrams: replace (source IP address, port #) of every outgoing datagram to (NAT IP address, new port #)
      remote clients/servers will respond using (NAT IP address, new port #) as destination address
  remember (in NAT translation table) every (source IP address, port #) to (NAT IP address, new port #) translation pair
  incoming datagrams: replace (NAT IP address, new port #) in destination fields of every incoming datagram with corresponding (source IP address, port #) stored in NAT table

## Slide 70: NAT: network address translation
S: 10.0.0.1, 3345
D: 128.119.40.186, 80
1
10.0.0.4
138.76.29.7
1: host 10.0.0.1 sends datagram to 128.119.40.186, 80
NAT translation table
WAN side addr LAN side addr
138.76.29.7, 5001 10.0.0.1, 3345
…… ……
S: 128.119.40.186, 80
D: 10.0.0.1, 3345
4
S: 138.76.29.7, 5001
D: 128.119.40.186, 80
2
2: NAT router changes datagram source address from 10.0.0.1, 3345 to 138.76.29.7, 5001,
updates table
S: 128.119.40.186, 80
D: 138.76.29.7, 5001
3
3: reply arrives, destination address: 138.76.29.7, 5001
10.0.0.1
10.0.0.2
10.0.0.3

## Slide 71
Table Addresses for private networks

## Slide 72: IPv6: motivation
initial motivation: 32-bit IPv4 address space would be completely allocated
additional motivation:
  speed processing/forwarding: 40-byte fixed length header
  enable different network-layer treatment of “flows”
IPv6 datagram format:
  fixed-length 40 byte header
  no fragmentation allowed

## Slide 73: IPv6: motivation
Fig: IPv6 Address Format

## Slide 74: IPv6: Addreviated Address

## Slide 75: IPv6: Addreviated Address

## Slide 76: IPv6: Addreviated Address

## Slide 77: IPv6 datagram format
payload (data)
destination address
(128 bits)
source address
(128 bits)
payload len
next hdr
hop limit
flow label
pri
ver
32 bits
priority: identify priority among datagrams in flow
flow label: identify datagrams in same "flow.”
128-bit
IPv6 addresses
What’s missing (compared with IPv4):
no checksum (to speed processing at routers)
no fragmentation/reassembly
no options (available as upper-layer, next-header protocol at router)

## Slide 78: Transition from IPv4 to IPv6
not all routers can be upgraded simultaneously
  no “flag days”
  how will network operate with mixed IPv4 and IPv6 routers?
IPv4 source, dest addr
IPv4 header fields
IPv4 datagram
IPv6 datagram
IPv4 payload
UDP/TCP payload
IPv6 source dest addr
IPv6 header fields
tunneling: IPv6 datagram carried as payload in IPv4 datagram among IPv4 routers (“packet within a packet”)
  tunneling used extensively in other contexts (4G/5G)

## Slide 79: Tunneling and encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
IPv4 network
IPv4 network connecting two IPv6 routers

## Slide 80: Tunneling and encapsulation
Ethernet connecting two IPv6 routers:
Ethernet connects two IPv6 routers
A
B
IPv6
IPv6
E
F
IPv6
IPv6
IPv4 tunnel connecting two IPv6 routers
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
E
F
IPv6
Link-layer frame
IPv6 datagram
The usual: datagram as payload in link-layer frame
IPv4 datagram
IPv6 datagram
tunneling: IPv6 datagram as payload in a IPv4 datagram
IPv6/v4
IPv6/v4

## Slide 81: Tunneling
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
physical view:
IPv4
IPv4
E
IPv6/v4
IPv6
F
C
D
A
B
IPv6
IPv6/v4
logical view:
IPv4 tunnel
connecting IPv6 routers
A
B
IPv6
IPv6/v4
E
F
IPv6/v4
IPv6
flow: X
src: A
dest: F
data
A-to-B:
IPv6
Flow: X
Src: A
Dest: F
data
src:B
dest: E
B-to-C:
IPv6 inside
IPv4
E-to-F:
IPv6
flow: X
src: A
dest: F
data
B-to-C:
IPv6 inside
IPv4
Flow: X
Src: A
Dest: F
data
src:B
dest: E
Note source and destination addresses!